## Slide 1: Bluetooth Controlled RC Car
College Expo Project
Team Members:
Siddharth S
Mohith J
Navienkumar C
Shri Shyam A J

## Slide 2: Introduction
• A Bluetooth-controlled RC car built using Arduino UNO
• Controlled wirelessly using a smartphone app
• Demonstrates integration of hardware and software in robotics

## Slide 3: Components Used
• Arduino UNO
• L298N Motor Driver
• 4 x 6V DC Motors
• 2 x Lithium-ion Batteries
• HC-05 Bluetooth Module
• Buzzer
• 4 x LEDs
• Jumper Wires
• Switch
• Mini bread board

## Slide 4: Working Principle
• The smartphone sends commands via Bluetooth
• Arduino UNO processes the received commands
• L298N motor driver controls the motors accordingly
• Car moves forward, backward, left, or right
• LEDs and buzzer used for indication

## Slide 5: Advantages
• Low-cost and easy to build
• Portable and battery-operated
• Wireless control using a smartphone
• Good learning project for robotics and IoT

## Slide 6: Applications
Wireless Control of Vehicles – It shows how Bluetooth can be used to remotely control cars, robots, or small vehicles.
Robotics & Automation – Useful in making mobile robots that can be guided wirelessly for tasks like delivery or surveillance.
Educational Purpose – Great for learning about Arduino, motor drivers, sensors, and wireless communication.
Prototyping for Smart Cars – Basic idea behind remote-controlled or even autonomous vehicle systems. Can be upgraded with sensors for advanced robotics

## Slide 7: Circuit Diagram

## Slide 8: Arduino Code (Part 1)
#include <AFMotor.h>
// Define motor pins
#define motorA1 7 // IN1
#define motorA2 6 // IN2
#define motorB1 5 // IN3
#define motorB2 4 // IN4
#define ENA 8 // PWM for motor A
#define ENB 3 // PWM for motor B
void setup() {
Serial.begin(9600); // Start Bluetooth communication
pinMode(motorA1, OUTPUT);
pinMode(motorA2, OUTPUT);
pinMode(motorB1, OUTPUT);
pinMode(motorB2, OUTPUT);
pinMode(ENA, OUTPUT);
pinMode(ENB, OUTPUT);
}

## Slide 9: Arduino Code (Part 2)
void loop() {
if (Serial.available()) {
char command = Serial.read(); // Read command from Bluetooth
controlMotors(command);
}
}
void controlMotors(char command) {
switch (command) {
case 'F': // Move Forward
digitalWrite(motorA1, LOW);
digitalWrite(motorA2, HIGH);
digitalWrite(motorB1, HIGH);
digitalWrite(motorB2, LOW);
analogWrite(ENA, 255); // Set speed (max)
analogWrite(ENB, 255); // Set speed (max)
break;
case 'B': // Move Backward
digitalWrite(motorA1, HIGH);
digitalWrite(motorA2, LOW);
digitalWrite(motorB1, LOW);
digitalWrite(motorB2, HIGH);
analogWrite(ENA, 255);
analogWrite(ENB, 255);
break;

## Slide 10: Arduino Code (Part 3)
case 'L': // Turn Left
digitalWrite(motorA1, LOW);
digitalWrite(motorA2, HIGH);
digitalWrite(motorB1, LOW);
digitalWrite(motorB2, HIGH);
analogWrite(ENA, 255);
analogWrite(ENB, 255);
break;
case 'R': // Turn Right
digitalWrite(motorA1, HIGH);
digitalWrite(motorA2, LOW);
digitalWrite(motorB1, HIGH);
digitalWrite(motorB2, LOW);
analogWrite(ENA, 255);
analogWrite(ENB, 255);
break;
case 'S': // Stop
digitalWrite(motorA1, LOW);
digitalWrite(motorA2, LOW);
digitalWrite(motorB1, LOW);
digitalWrite(motorB2, LOW);
break;
default: // Default case
break;
}
}

## Slide 11: Software Used
• Arduino IDE
• Tinkercad
Arduino IDE: Arduino IDE (Integrated Development Environment) is the official software used to write, compile, and upload programs (sketches) to Arduino boards. It supports C/C++ and provides libraries for sensors, motors, and communication modules.
Tinkercad: Tinkercad is an online simulation and circuit design tool developed by Autodesk. It allows users to design circuits, simulate Arduino projects, and test code without physical hardware.

## Slide 12: Conclusion
This project demonstrates the use of Arduino and Bluetooth in building a simple RC car.
It provides practical knowledge in embedded systems, wireless communication, and robotics.
-- PPT by S Sajjan